## Slide 1: NaaS box application specific middlebox
University of Cambridge
Imperial College London
University of Nottingham

## Slide 2: NaaS box: application specific middlebox
Performance:
  Line rate data processing (10G initially)
  Efficient use of network resources
  Offload to hardware
Flexibility:
  Very rapid development for new applications
  Simple deployment, resource placement and resource allocation
Security:
  Isolation of applications within shared hardware

## Slide 3: NaaS box basics
Generalise the concept of NetAgg to a general application specific middlebox. Example apps:
  Hadoop reduce (as in NetAgg)
  Graph processing
  Web proxy
  Memcached
  Deep learning (neural nets)
Rapid development of apps, exploit natural data parallelism

## Slide 4: Core concepts
Domain Specific High-Level Language:
  Adding new applications to middlebox is easy
  Compiler not programmer takes care of parallelism
  Language guarantees performance bounds
Task elements linked in Task Graph:
  Parallel computation as natural isolated units
  Scheduling of execution guarantees application fairness and efficiency

## Slide 5: Core concepts: DS HLL
Domain specific high-level language for user compiles to C++
Easy to write, specific to middlebox tasks
Non Turing complete – express only transforms that will run at line rate
http_response response =
send(value = input, host = desthost)
send(value = response, host = source)

## Slide 6: DS HLL webproxy example
type http_request : record
header : record
...
method : variant
...
host desthost[noHosts] = ...
void main (config cfg, host source, http_request input):
static host desthost = null
if desthost == null:
desthost = tcphost[hash(input.url) % noHosts]
http_response response =
send(value = input, host = desthost)
send(value = response, host = source)
Type declaration implies
Serialiser/deserialiser
Type of input implies number/nature of streams
Simple hash – splits traffic
equally to hosts
send built in implies structure of task graph

## Slide 7: DS HLL goals
Static code analysis for performance guarantees
Serialise/Deserialise of wire data inferred from types
Parallelism inferred from language, compiler makes choices about task graph
All c0nfiguration information for that application in one place

## Slide 8: Core concepts: Task graph
Task graph maps N data-stream inputs to M outputs
Streams are broken to chunks for processing (e.g. web request, Hadoop reduce)
Task elements (nodes) connected by channels (edges)
Graphs dynamically created/destroyed as needed
Scheduling ensures fairness between applications
Compiler infers graph from HLL

## Slide 9: Task graph: Web proxy example
Load balancing web server: http GET/RESPONSE returned from single server chosen from pool
Serialise/deserialise slices input into get requests
New TCP connection -> new WebProxyTaskGraph
Two graphs, out and return path
On first call blue element selects which server to use and connects output task to correct server
GET
GET
RESP.
RESP.

## Slide 10: Core concepts: Dispatching and scheduling
ApplicationDispatcher: listens on a given socket
  Existing connections pass data to input task
  New connections passed to graph dispatcher
GraphDispatcher: connect TCP streams to input tasks correctly (perhaps create new Task Graph)
Scheduler: picks Task Elements to run (fairness between apps, efficiency of scheduling)
?
?

## Slide 11: Implementation details
Core code – C++
Networking DPDK (Datapath development kit) for bitshifting from NIC
mTCP for userland TCP stack
Current code runs at near 10G on our testbed in simple test applications
However more advanced apps will take more CPU time – more code “tweaking” required.

## Slide 12: Summary: NaaS box basics
Core component of system – the middlebox itself
Ongoing design – first “usable” draft mid 2015.
Flexible usage multiple applications on one box
Combined with:
  NetFGPA (heavy lifting on network side)
  SDN control (resource placement + allocation)
See next presentations for details

## Slide 13: Reserve slides