## Slide 1: EPSRC NaaS Project: Network-as-a-Service
University of Cambridge
Imperial College London
University of Nottingham
Funded by the UK Engineering and Physical Sciences Research Council (EPSRC)
Peter Pietzuch, Imperial College London <prp@doc.ic.ac.uk>

## Slide 2: Problem Statement
Network often limits
performance of data centre applications
Modern applications have complex network requirements
Cloud data centres

## Slide 3: Bridging the Application/Network Gap
Application perspective
Network perspective
Network only sees packets
No insights about application requirements
10.0.1.4
10.0.2.3
Applications only see IP addresses
  Hard to infer locality & congestion
No control over packet routing
?
?
Why slow?
Are these related?
Applications have little control over the network (and vice versa)

## Slide 4: Letting Applications Adapt the Network
Many proposals for software-based routers and switches
  e.g. OpenFlow, RouteBricks , ServerSwitch, PacketShader, NetMap,…
  Programmable hardware for networking, eg NetFPGAs, ...
Focus on traditional application-agnostic network services
  e.g. IPv4 forwarding, deep packet inspection, firewalls
Why don’t we implement application-specific services?
  e.g. in-network aggregation, caching, load balancing, content-based routing, ...
NaaS Goal: Abstractions & mechanisms to enable applications to efficiently, easily and safely process data within the network

## Slide 5: NaaS Project Vision
Exploit programmability of network devices for application-specific processing
NaaS Boxes process data at line rate in network

## Slide 6: Challenges for NaaS
1. Performance & efficiency
  Line rate data processing (10Gbps initially)
  Efficient use of network resources
  Offload to hardware when possible
2. Programmability & flexibility
  Rapid development of new network services
  Simple deployment, resource placement and allocation
3. Security & safety
  Isolation of services within shared hardware

## Slide 7: A. NaaS Box Architecture
Software platform for application-specific middlebox services
  eg application-specific load-balancing, in-network computation, ...
Services written in high-level DSL compiled to C++
  Services parallelised as cooperatively-scheduled task graphs across CPU cores
Services “safe by design”  safety & performance guarantees

## Slide 8: B. Hardware-Assisted NaaS Box
Hard to achieve 10Gbps line rate in software alone
   Push certain features into hardware (NetFPGA)
NetFPGA as TCP endpoint and basic per-app processing
  eg serialisation/deserialisation of payload data
  Aids processing  frees CPU cores for other tasks

## Slide 9: C. SDN-Controlled NaaS
Distributed, reliable, application-aware SDN controller
SDN controller redirects app traffic via appropriate NaaS box
  Initially based on OpenFlow
  Directs queries to appropriate NaaS box for application
  Balances both traffic and load on NaaS boxes

## Slide 10: Meeting Agenda
10:50 NaaS project overview (Peter Pietzuch)
11:05 Progress to date: ”NetAgg: On-path aggregation” (Paolo Costa)
11:25 Progress to date: ”Mirage/OpenFlow” (Masoud Koleini)
11:45 Industrial Partner presentations: Netronome
12:00 Industrial Partner presentations: Xilinx
12:15 Industrial Partner presentations: Citrix
12:30 Industrial Partner presentations: BT
12:45 Industrial Partner presentations: NetApp
13:00 Lunch
14:00 Ongoing: “NaaS Box: Application-specific middleboxes” (Richard Clegg)
14:30 Ongoing: “NetFPGA DMA engine” (Nik Sultana)
15:00 Ongoing: “Mirage SDN switching and control” (Richard Mortier)
15:30 Coffee break
15:45 Progress summary/next steps (Alex Wolf)
16:30 End of meeting