## Slide 1: NaaS: Mirage SDN, Switching and Control
University of Cambridge
Imperial College London
University of Nottingham
Funded by the UK Engineering and Physical Sciences Research Council (EPSRC)
Richard Mortier, University of Nottingham^WCambridge
<richard.mortier@cl.cam.ac.uk>

## Slide 2: Challenges for NaaS
Performance & efficiency
  Line rate data processing (10Gbps initially)
  Efficient use of network resources
  Offload to hardware when possible
Programmability & flexibility
  Rapid development of new network services
  Simple deployment, resource placement and allocation
Security & safety
  Isolation of services within shared hardware

## Slide 3: Current Directions
A key piece of NaaS is flexibility: how can applications better use network resources?
OpenFlow Alternatives
  P4, POF
Raising the abstraction
  Above the transport layer
Self-scaling applications
  Distributed control

## Slide 4: OpenFlow Alternatives
OpenFlow has limitations:
  Standard continues to expand (12 to 41 fields)
  Fixed header fields limits experimentation
  Extensible match fields provide substrate for extensibility
Interested in investigating alternatives
  E.g., Protocol Oblivious Forwarding (Huawei), P4 (Bosshart et al, http://arxiv.org/pdf/1312.1719.pdf)

## Slide 5: Emphasising Extensibility
POF (Huawei)
  Multi-level table matching
  (Pointer, Offset), pointer guaranteed to advance
P4 (Barefoot, Intel, Stanford, MSR, Google, Princeton)
  “Parse and populate” model
  Programmable parser, parallel matching
  Actions composed of protocol independent switch primitives
How do these alternatives compare, and are they sufficient for our needs?

## Slide 6: Raising the Abstraction
OpenFlow focuses on packets and flows
  The usual Ethernet and IP headers (incl. IPv6)
  Plus some support for key control protocols (ARP, DHCP, MPLS, VLAN)
  Plus statistics messages
But applications deal in Layer 8 behaviour
  Mirage applications link SDN libraries directly
  How will applications use them?
How can we raise abstractions so that applications can deal in layer 8 concepts (e.g., URLs)?

## Slide 7: Self-Scaling Applications
Use of the network by applications is rather naïve
  The network as a black box
  Little to no direct control
SDN allows us to go further
  Applications install handlers to deal with particular sets of network traffic
How can we take this further, enabling application logic to modify its own deployment – e.g., scaling up/down in response to load – in light of network conditions?

## Slide 8: Scaling Out: Jitsu

## Slide 9: Conduit: Efficient Inter-VM Comms
Zero-copy shared-memory pages between peers
  Xen grant tables map pages between VMs, synchronised via event channels
  Rendezvous facility so VMs discover named peers
  Supports unikernel and legacy VM rendezvous
  Hooks into higher-level name services like DNS
Compatible with the vchan inter-VM communication protocol

## Slide 10: Conduit: XenStore Layout

## Slide 11: Jitsu Directory Service
Performs the role of Unix's inetd:
  Jitsu VM launches at boot time to handle name resolution (whether local via a well known jitsud Conduit node in XenStore or remote via DNS)
  When a request arrives for a live unikernel, Jitsu returns the appropriate endpoint
  If the unikernel is not live, Jitsu boots it, and acts as proxy until the unikernel is ready

## Slide 12: Result: Low Latency Boot
350ms VM Boot (ARM)
20ms VM Boot (x86)

## Slide 13: Synjitsu: Masking Latency
By buffering TCP requests into XenStore and then replaying, Synjitsu parallelises connection setup and unikernel boot

## Slide 14: Summary
So current themes are focused on investigating several ways to improve flexibility
Replacing OpenFlow
Raising the level of abstraction
Automating datacenter deployment